## Slide 1: Essential SmartBright G3 LED Floodlight
Presenter’s name
Sep 2018

## Slide 2
Application 应用场景
Amenity
Landscape
Area
Bill board
Parking
Architectural

## Slide 3
The Essential SmartBright G3 LED floodlight comes with a compact and sturdy design. Its light weight with die-cast aluminum housing and corrosion-proof powder coating, suitable for general outdoor application. High efficiency designed with latest LED technology, achieves substantial energy savings comparing to conventional floodlights.
General introduction 介绍
Features and Benefits
• Ideal replacement for conventional halogen floodlight
• Reliable quality guarantee hassle free for outdoor application
• Robust die-cast aluminum housing
• Energy saving

## Slide 4
Type | BVP150 |  |  |  | 
lumen output | 850 lm | 1700 lm | 2550 lm | 4250 lm | 5950lm
Power | 10W | 20W | 30W | 50W | 70W
PF | >0.9 |  |  |  | 
SDCM | <7 |  |  |  | 
CRI | 80 |  |  |  | 
CCT | 3000K / 4000K / 6500K |  |  |  | 
Light distribution | SWB(110°) |  |  |  | 
Voltage | 220-240V~ 50/60Hz |  |  |  | 
Surge protection | 1KV/2KV |  |  |  | 
LED driver | DoB design (driver on board) |  |  |  | 
Connection | 300mm flying cable |  |  |  | 500mm flying cable
Materials and finishing | Die-cast aluminum housing(black), Textured tempered glass |  |  |  | 
Lifetime | 20,000 hours (L70B50@25°C) |  |  |  | 
Working Temp. | - 40°C < Ta < +50°C |  |  |  | 
Dimension W x H x D(mm) | 115x92x28 | 140x110x28 | 170x130x29 | 200x145x33 | 245x185x36
Electrical Class | Class I |  |  |  | 
IP / IK rating | IP65 / IK06 |  |  |  | 
Certifications | CQC, CE, CB, EMC |  |  |  | 
Proudct Specification 产品参数

## Slide 5
一体化铭牌，增加仿冒难度
Philips logo embarked, stands out
压铸铝壳体，牢固可靠
Reliable die-cast aluminum housing
带质地钢化玻璃罩，安全美观
Textured tempered glass; elegant but sturdy
DoB 设计，纤巧紧凑
Driver on board design, compact & slim
通过严格的安全及可靠性测试，符合CQC标准。
即使在-40度低温，50度的高温或者高湿度的环境下反复开关测试，表现依旧稳定
The product passes national and international test requirement, and it’s able to operate in wide ambient temperature range from -40°C to +50°C.

## Slide 6
Dimesions 产品尺寸

## Slide 7
Packaging 产品包装
Type 型号 | MPQ 装箱量
10W | 20 in 1
20W | 15 in 1
30W | 15 in 1
50W | 6 in 1
70W | 6 in 1
- Product comes with individual color box
-Multiple individual color box inside one brown box

## Slide 8
Order information 订购信息 – For Growth Markets
12nc | Description | Power | CCT | Light distribution | MPQ | MoQ
911401732322 | BVP150 LED8/WW 220-240V 10W SWB CE | 10 | 3000K | SWB (110°) | 20 | 200
911401732332 | BVP150 LED8/NW 220-240V 10W SWB CE | 10 | 4000K | SWB (110°) | 20 | 200
911401732342 | BVP150 LED8/CW 220-240V 10W SWB CE | 10 | 6500K | SWB (110°) | 20 | 200
911401732352 | BVP150 LED17/WW 220-240V 20W SWB CE | 20 | 3000K | SWB (110°) | 15 | 150
911401732362 | BVP150 LED17/NW 220-240V 20W SWB CE | 20 | 4000K | SWB (110°) | 15 | 150
911401732372 | BVP150 LED17/CW 220-240V 20W SWB CE | 20 | 6500K | SWB (110°) | 15 | 150
911401732382 | BVP150 LED25/WW 220-240V 30W SWB CE | 30 | 3000K | SWB (110°) | 15 | 150
911401732392 | BVP150 LED25/NW 220-240V 30W SWB CE | 30 | 4000K | SWB (110°) | 15 | 150
911401732402 | BVP150 LED25/CW 220-240V 30W SWB CE | 30 | 6500K | SWB (110°) | 15 | 150
911401732412 | BVP150 LED42/WW 220-240V 50W SWB CE | 50 | 3000K | SWB (110°) | 6 | 120
911401732422 | BVP150 LED42/NW 220-240V 50W SWB CE | 50 | 4000K | SWB (110°) | 6 | 120
911401732432 | BVP150 LED42/CW 220-240V 50W SWB CE | 50 | 6500K | SWB (110°) | 6 | 120
911401732442 | BVP150 LED59/WW 220-240V 70W SWB CE | 70 | 3000K | SWB (110°) | 6 | 120
911401732452 | BVP150 LED59/NW 220-240V 70W SWB CE | 70 | 4000K | SWB (110°) | 6 | 120
911401732462 | BVP150 LED59/CW 220-240V 70W SWB CE | 70 | 6500K | SWB (110°) | 6 | 120

## Slide 10: Essential SmartBright G3 LED Floodlight
Presenter’s name
Sep 2018

## Slide 11
Application 应用场景
Amenity
Landscape
Area
Bill board
Parking
Architectural

## Slide 12
明欣LED第二代投光灯BVP150泛光照明灯具采用了更加紧凑设计，与上一代相比较外形更加纤巧，铝压铸壳体，坚固耐用。防腐蚀粉末涂层，确保产品可以在户外应用。更先进的LED科技，更高的系统光效，节能更显著，可以用来替代上一代灯具以及传统泛光灯具，实现可持续发展。
亮丽柔和 舒适感受
出光柔和舒适；重新新设计的
带质地的钢化玻璃面罩，增加美观，并降低眩光对眼睛的刺激
轻巧灵活 美观简洁
超薄集成式设计，更加紧凑，
极好地降低灯具的曝光，见光不见灯
设计精良 安全可靠
高品质压铸铝外壳，防水防
尘防冲击，适用在宽范围温
度变化的环境
经久耐用 经济节能
比上一代提升效率，更加节能，替代QVF卤素投光灯，长效免维护，降低使用成本

## Slide 13
一体化铭牌，增加仿冒难度
Philips logo embarked, stands out
压铸铝壳体，牢固可靠
Reliable die-cast aluminum housing
带质地钢化玻璃罩，安全美观
Textured tempered glass; elegant but sturdy
DoB 设计，纤巧紧凑
Driver on board design, compact & slim
通过严格的安全及可靠性测试，符合CQC标准。
即使在-40度低温，50度的高温或者高湿度的环境下反复开关测试，表现依旧稳定
The product passes national and international test requirement, and it’s able to operate in wide ambient temperature range from -40°C to +50°C.

## Slide 14
Type | BVP150 |  |  |  | 
lumen output | 850 lm | 1700 lm | 2550 lm | 4250 lm | 5950lm
Power | 10W | 20W | 30W | 50W | 70W
PF | >0.9 |  |  |  | 
SDCM | <7 |  |  |  | 
CRI | 80 |  |  |  | 
CCT | 2400K / 3000K / 4000K / 6500K |  |  |  | 
Light distribution | SWB(110°) |  | SWB(110°); AWB(30°x80°) |  | 
Voltage | 220-240V~ 50/60Hz |  |  |  | 
Surge protection | 1KV/2KV |  |  |  | 
LED driver | DoB design (driver on board) |  |  |  | 
Connection | 300mm flying cable |  |  |  | 500mm flying cable
Materials and finishing | Die-cast aluminum housing(black), Textured tempered glass |  |  |  | 
Lifetime | 20,000 hours (L70B50@25°C) |  |  |  | 
Working Temp. | - 40°C < Ta < +50°C |  |  |  | 
Dimension W x H x D(mm) | 115x92x28 | 140x110x28 | 170x130x29 | 200x145x33 | 245x185x36
Electrical Class | Class I |  |  |  | 
IP / IK rating | IP65 / IK06 |  |  |  | 
Certifications | CQC, CE, CB, EMC |  |  |  | 
Proudct Specification 产品参数

## Slide 15
Dimesions 产品尺寸

## Slide 16
Packaging 产品包装
Type 型号 | MPQ 装箱量
10W | 20 in 1
20W | 15 in 1
30W | 15 in 1
50W | 6 in 1
70W | 6 in 1
- Product comes with individual color box
-Multiple individual color box inside one brown box

## Slide 17
Order information 订购信息 – For China Market
12nc | Description | Power | CCT | Light distribution | MPQ | MoQ
911401732562 | BVP150 LED8/2400K 220-240V 10W SWB CQC | 10 | 2400K | SWB (110°) | 20 | 200
911401732612 | BVP150 LED8/WW 220-240V 10W SWB CQC | 10 | 3000K | SWB (110°) | 20 | 200
911401732622 | BVP150 LED8/NW 220-240V 10W SWB CQC | 10 | 4000K | SWB (110°) | 20 | 200
911401732632 | BVP150 LED8/CW 220-240V 10W SWB CQC | 10 | 6500K | SWB (110°) | 20 | 200
911401732572 | BVP150 LED17/2400K 220-240V 20W SWB CQC | 20 | 2400K | SWB (110°) | 15 | 150
911401732642 | BVP150 LED17/WW 220-240V 20W SWB CQC | 20 | 3000K | SWB (110°) | 15 | 150
911401732652 | BVP150 LED17/NW 220-240V 20W SWB CQC | 20 | 4000K | SWB (110°) | 15 | 150
911401732662 | BVP150 LED17/CW 220-240V 20W SWB CQC | 20 | 6500K | SWB (110°) | 15 | 150
911401732582 | BVP150 LED25/2400K 220-240V 30W SWB CQC | 30 | 2400K | SWB (110°) | 15 | 150
911401732672 | BVP150 LED25/WW 220-240V 30W SWB CQC | 30 | 3000K | SWB (110°) | 15 | 150
911401732682 | BVP150 LED25/NW 220-240V 30W SWB CQC | 30 | 4000K | SWB (110°) | 15 | 150
911401732692 | BVP150 LED25/CW 220-240V 30W SWB CQC | 30 | 6500K | SWB (110°) | 15 | 150
911401732592 | BVP150 LED42/2400K 220-240V 50W SWB CQC | 50 | 2400K | SWB (110°) | 6 | 120
911401732702 | BVP150 LED42/WW 220-240V 50W SWB CQC | 50 | 3000K | SWB (110°) | 6 | 120
911401732712 | BVP150 LED42/NW 220-240V 50W SWB CQC | 50 | 4000K | SWB (110°) | 6 | 120
911401732722 | BVP150 LED42/CW 220-240V 50W SWB CQC | 50 | 6500K | SWB (110°) | 6 | 120
911401732602 | BVP150 LED59/2400K 220-240V 70W SWB CQC | 70 | 2400K | SWB (110°) | 6 | 120
911401732732 | BVP150 LED59/WW 220-240V 70W SWB CQC | 70 | 3000K | SWB (110°) | 6 | 120
911401732742 | BVP150 LED59/NW 220-240V 70W SWB CQC | 70 | 4000K | SWB (110°) | 6 | 120
911401732752 | BVP150 LED59/CW 220-240V 70W SWB CQC | 70 | 6500K | SWB (110°) | 6 | 120
911401732762 | BVP150 LED25/WW 220-240V 30W AWB CQC | 30 | 3000K | AWB (30°X80°) | 15 | 150
911401732772 | BVP150 LED25/NW 220-240V 30W AWB CQC | 30 | 4000K | AWB (30°X80°) | 15 | 150
911401732782 | BVP150 LED25/CW 220-240V 30W AWB CQC | 30 | 6500K | AWB (30°X80°) | 15 | 150
911401732792 | BVP150 LED42/WW 220-240V 50W AWB CQC | 50 | 3000K | AWB (30°X80°) | 6 | 120
911401732802 | BVP150 LED42/NW 220-240V 50W AWB CQC | 50 | 4000K | AWB (30°X80°) | 6 | 120
911401732812 | BVP150 LED42/CW 220-240V 50W AWB CQC | 50 | 6500K | AWB (30°X80°) | 6 | 120
911401732822 | BVP150 LED59/WW 220-240V 70W AWB CQC | 70 | 3000K | AWB (30°X80°) | 6 | 120
911401732832 | BVP150 LED59/NW 220-240V 70W AWB CQC | 70 | 4000K | AWB (30°X80°) | 6 | 120
911401732842 | BVP150 LED59/CW 220-240V 70W AWB CQC | 70 | 6500K | AWB (30°X80°) | 6 | 120